## Slide 1
N
e
w
E
n
g
l
a
n
d
T
r
a
n
s
p
o
r
t
a
t
i
o
n
C
o
n
 | FACT SHEET
 | Framework of Asphalt Balanced Mix Design (BMD) for New England Transportation Agencies
RESEARCH PROJECT TITLE Framework of Asphalt Balanced Mix Design (BMD) for New England Transportation Agencies STUDY TIMELINE February 2019 – December 2020 PRINCIPAL INVESTIGATOR Dr. Walaa S. Mogawer, P.E. - PI Dr. Thomas Bennert NETC CONTACT Kirsten Seeber NETC Coordinator CTC & Associates LLC 608-620-5820 netc@ctcandassociates.com MORE INFORMATION NETC Coordinator will add link to the final report on NETC website The New England Transportation Consortium, a cooperative effort of the transportation agencies of the six New England States, funded this research. Through the Consor- tium, the states pool professional, academic and financial resources for transportation research leading to the development of improved methods for dealing with com- mon problems associated with the administration, planning, design, construction, rehabilitation, recon- struction, operation and mainte- nance of the region’s transporta- tion system. | Introduction Superpave volumetric design method as outlined in AASHTO M323 “Standard Specification for Superpave Volumetric Mix Design” is currently being used by New England state transportation agencies to design their asphalt mixtures, specifically dense graded mixtures. A concern with this design method is that the volumetric design alone does not measure, quantify or predict mixture performance prior to placement. Forecasting mixture performance is desired by many state transportation agencies due to many recent developments in the asphalt paving industry including: utilization of binders formulated with various modifiers versus conventionally neat asphalt binders, the incorporation of more recycled materials into mixtures, and utilization of new technologies. Mixtures designed with respect to these factors have unknown performance as Superpave was never designed to compensate for them. This has led to an increased interest in developing a performance-related specification using a balanced mixture design (BMD) concept. BMD incorporates two or more performance tests to evaluate how well a mixture will resist certain distresses that are of concerns for a particular state transportation agency. To date, there have been no regionally based studies to investigate this approach with respect to the typical distress issues and materials in New England. The objective of this study was to synthesize existing information and to develop recommendations for a rational BMD approach for use by New England transportation agencies. Methodology A survey was developed and administered to ascertain information related to pavement distress for the New England transportation agencies as well as to determine the potential roadblocks to BMD implementation. Based on the distresses noted in the survey, candidate asphalt mixture performance tests were identified and the pros and cons of each test were outlined in relation to existing availability, equipment cost, and testing time. Performance testing equipment currently housed by each agency, as well as past or current research work the agencies have conducted with different test devices was inventoried in a separate survey. Available field and laboratory performance data for asphalt mixtures were collected from the state agencies to conduct an in-depth analysis to develop preliminary BMD criteria individualized for each state. Conclusion The predominate asphalt mixture distresses noted in the survey were thermal and fatigue cracking. Candidate performance were presented for the New England transportation agencies for rutting, fatigue cracking, thermal cracking and moisture damage. The potential roadblocks to BMD implementation were identified as time to procure performance test equipment and difficulties in procuring calibration and repair services for said equipment. Methods to establish performance criteria for BMD were outlined including using pavement management system (PMS) data and “historical” or “existing visual” field performance. Using these methods, and available field and laboratory data from three state agencies, initial state specific performance criteria for BMD and performance related specification were developed. The criteria were different for each state as the availability of data varied. What are potential impacts? The study results provide the BMD current state-of-practice and a roadmap for each agency to follow in their BMD implementation efforts at the state and regional level. Knowledge gaps were identified and recommendations for future research were presented to outline the work still needed to advance BMD implementation. Ultimately, using BMD will results in better performing (longer lasting) roads being constructed and optimized use of already limited funding.